SPECIFICATION SHEET

# MACHINE		: - Ajax Evolution AJEV200 CNC Teach Lathe

Stock No		: - 9022

# PRICE			: - £6,750.00 + VAT

Serial No		: - 52249

Control		: - Fanuc OiMate TC

Date of Manufacture	: - 2004

SPECIFICATION

Capacity

Centre height				200mm

Centre distance				1000mm

Swing over bed				400mm

Swing over carriage			370mm

Swing over cross slide			210mm

Bed width				300mm

Headstock

Main spindle bore			65mm

Main spindle nose			Camlock - n°6

Main spindle morse taper		5

Number of speeds			2

st		0-675

(turns/minute)		2nd range	675-3.000

Feeds

Working feed Z, X			0-10,000mm/min

Rapid traverse Z, X			10m/min

Tailstock

Tailstock barrel diameter		68mm

Tailstock barrel travel			220mm

Tailstock taper				4mm

Motors

Main motor power 			7.5Kw

General

Dimensions				2600 x 1350mm

Weight					1130kg

Complete with:-

10” chuck

Automatic toolpost

Rear quick change toolpost

Manual

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.