SPECIFICATION SHEET

# MACHINE	: - Used Feeler VMP-580APC Twin Pallet Vertical Machining Centre

Stock No		: - 9202

# PRICE			: - £35,000.00 + VAT

Serial No		: - VKCAP119

Control		: - Fanuc Oi-MD CNC Control System

Date of Manufacture	: - 2012

SPECIFICATION

Capacity

X axis travel					580mm

Y axis travel					420mm

Z axis travel					510mm

Table size					580 x 410mm

Allowable table load				120kg

Table clamping spacing x width			35-M12 x P1. 75

Spindle

Spindle nose to table top			135 – 645mm

Spindle centre to column			455mm

Spindle taper					ISO No. 40

Spindle speed					12,000 RPM

AC spindle motor (30 minutes)			11.kW (15HP)

Spindle torque (30 minutes)			56 Nm

Automatic Pallet Changer (APC)

No. of pallets					2PCS

Pallet movement type				Swing arm

Pallet size					580 x 410mm

Max load capacity				120kgs

Air clamping force				1046 kgs

Cylinder diameter				150mm

Rod diameter					100mm

Pallet change time				6 sec

Note: - Positioning type at working area. Hydraulic clamping with 4 taper cones combined with positioning air blast at pallet station with lock pin

Automatic Toolchanger

Number of tools				24

Tool shank					BT 40 Big Plus

Pull stud					JIS B. 6339

Maximum tool diameter				80mm

With empty adjacent pockets			130mm

Maximum tool length				250mm

Maximum tool weight				7kg

Tool to tool change time			2.2 secs

Chip to chip change time			3.8 secs

Motion

X and Y axis rapid traverse rate			48m/min

Z axis rapid traverse rate			48m/min

Maximum cutting feed rate			20000mm/min

Least command increment			0.001

X, Y & Z axis servomotors H. P.		2.1/4.0/5.4

X, Y & Z axis ballscrew diameter		32mm

Accuracy

Positioning accuracy (X, Y and Z axis)		0.009mm

Repeatability (X, Y and Z axis)			+/- 0.006mm

Note: - Geometric accuracies are only guaranteed if the machine is installed on foundation meeting the minim requirements of the machine. Contact Feeler UK for the current machine requirements.

General

Machine height					2375mm

Machine length					2630mm

Machine width					1900mm

Machine net weight				3900kg

Power required					20 KVA

Voltage required				400 ±10%

Standard Machine Equipment

Spindle chiller unit

30 bar through the spindle coolant preparation

Portable manual pulse generator

Program and data protection key switch

Spindle coolant ruing

Base flush chip disposal

Fully enclosed work area (including top)

Flood coolant

Work light

3 colour tower signal light

Auto power off

Extra set of 8M codes

Automatic lubrication unit

Hydraulic clamping interface

RJ45 socket (Ethernet)

Fanuc CNC Options Included

Fanuc Oi-MD Control Features

Specifications:

High resolution 8.4” colour display

32 bit microprocessor and data bus

Part program and data protection key switch

Subprogram call – 4 folds nested

Up to 200 registered programs

PCMCIA card slot

Standard Programming Features:

4 simultaneously controlled axes

Cutter compensation C (G40-42)

Tool length compensation (G43, 44, 49)

Least programmable increment: 0.001

Circular interpolation by radius designation

Background editing

Input/output interface (RS232C)

Reference point return (G27-G30)

Inch/metric conversion/programming

Rigid tapping

Decimal point programming

Programmable data input G10

Custom macro variable additional (total 600)

Absolute/incremental programming (G90, 91)

Tool life management

Helical interpolation

Copy and merge edit functions (expanded edit)

Custom B macro

Canned cycles for drilling, boring and tapping (G73, 74, 76, 80-89)

Standard Operation Features:

Tool offsets pair (200 total offsets)

Mirror image

Tool offset memory C (D/H, Geo/Wear)

Backlash compensation

Stored pitch error compensation

Program protect

Self-diagnostic functions

Keyboard type manual data input (MDI)

Run hour and parts count display

Manual pulse generator

Rapid traverse override

Feed per minute/feed per revolution

Automatic acceleration/deceleration

Federate override

Advance preview control

Spindle speed override

Skip function (G31)

Jog override

Coordinate system setting (G92)

Jog feed

Work coordinate system additional (P1-P48)

Coolant and Swarf Management

Scrape type swarf conveyor with 1050mm discharge height

5 bar pressure coolant system to spindle nozzles

5 bar pressure coolant system to bed wash

Probing System

Blum measurement system TC50 with infrared transmission

Complete with:-

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.