SPECIFICATION SHEET

# MACHINE		: - Used Haas Model VF1 Vertical CNC Machining Centre

Stock No		: - 9216

# PRICE			: - POA

Serial No		: - 1087406

Control		: - Haas (Fanuc compatible) CNC Control system

Date of Manufacture	: - 2011

SPECIFICATION

Travel

X axis stroke				508mm

Y axis stroke				406mm

Z axis stroke				508mm

Distance spindle nose to table		102-610mm

Table

Width					356mm

Length					660mm

Max. Weight on table			1361kg

T Slots:	 width				16mm

: pitch				125mm

Spindle

Taper size				No.40

Speed					0-10,000rpm

Bearings

Bearing lubrication			Air/oil injection

Cooling					Liquid cooled

Motor

Spindle motor, max. rating		22.4kW

Feedrate

Rapid X, Y & Z axis 			25.4m/min

Max. Cutting feedrate			16.5m/min

Toolchanger

Capacity				20 tools

Type					BT40

General

Approximate machine weight		3220kg

Air supply (min)			113lpm, 6.9 bar

Complete with: -

Programmable coolant nozzle

Automatic lubrication system

Enclosed guarding

Swarf auger

Lighting

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.