SPECIFICATION SHEET

# MACHINE		: - Mazak Hyper Quadrex 150MSY Multi Axis Turning Centre

Stock No		: - 9208

# PRICE			: - P. O. A

Serial No		: - 258360

Control		: - Mazatrol Matrix 2 CNC Control

Date of Manufacture	: - 2014 Installed 2015

SPECIFICATION

Capacity

Chuck size					6”

Maximum swing (upper turret)			320mm

Maximum swing (lower turret)			270mm

Standard machining diameter			242mm

Maximum machining diameter (upper turret)	300mm

Maximum machining diameter (lower turret)	170mm

Maximum support weight (1st spindle)		200kgf

Maximum support weight (2nd spindle)		150kgf

Maximum bar size diameter			65mm

Spindle

Rotating speed maximum (1st spindle)		5000 minˉ¹

Rotating speed maximum (2nd spindle)		6000 minˉ¹

Rotating speed minimum (1st spindle)		35 minˉ¹

Rotating speed minimum (2nd spindle)		35 minˉ¹

Acceleration (1st spindle)			2.70s

Acceleration (2nd spindle)			3.80s

Spindle nose (1st spindle)			A2-6”

Spindle nose (2nd spindle)			A2-5”

Spindle through hole diameter (1st spindle)	76mm

Spindle through hole diameter (2nd spindle)	61mm

Motor output (30-minute rating) (1st spindle)	15.0kW

Motor output (30-minute rating) (2nd spindle)	11kW

Motor output (continuous rating) (1st spindle)	11.0kW

Motor output (continuous rating) (2nd spindle)	8kW

Upper Turret

No of tools					12

Tool size (OD turning)				20mm

Tool size (ID turning)				32mm

Indexing time (single step)			0.20s

Indexing time (full turn)				0.6s

Mill speed rotating maximum			6000 minˉ¹

Mill spindle rotating speed minimum		35 minˉ¹

Mill spindle output (10-minute rating)		5.5kW

Lower Turret

No of tools					12

Tool size (OD turning)				20mm

Tool size (ID turning)				32mm

Indexing time (single step)			0.20s

Indexing time (full turn)				0.60s

Feed Axes

Travel X1 axis					175mm

Travel X axis (lower)				111mm

Travel Z1 axis					520mm

Travel Z2 axis					580mm

Rapid traverse (upper) X			30m/min

Rapid traverse (upper) Y			26m/min

Rapid traverse (upper) Z			40m/min

Rapid traverse (lower) X			24m/min

Rapid traverse (lower) Y			20m/min

Rapid traverse (lower) Z			40m/min

Others

Coolant tank capacity (total)			205 L

Power requirement (30-minute rating)		50.2kVA

Power requirement (continuous)			39.40kVA

NC Controller Options

EIA/ISO code input function

Spiral

EIA 3D Comp

Rotation

Geometric

Scaling

Ext -Data I/O

Threading function. Feed of the tool synchronised with spindle rotation is controlled. Thus, equal lead straight threading and tapered threading are possible. Also, multiple thread screws can be machine by designating the starting angle of threading (G33)

Sub C Axis Control

Main and secondary spindle synchronization to facilitate workpiece transfer without need to sop spindles

Inverse Time

Auto TLM

Polar coordinates input (G122)

Sequence number comparison stop function. The machine will come to block stop if code M)1 is set during automatic operation with the optional stop menu item remaining displayed in its reverse status.

G54.1

Milling spindle synchronous tapping. Fast and highly accurate machining becomes possible with tapping that fully synchronises with the revolutions of the milling spindle

User macro (600 variable)

Cylinder

EIA Helical Tap Cycle

EIA Pattern Cycle

Tilted Working Plane

Lower Turret Mazatrol

Mazak tapping/boring tornado (EIA)

Background tool path check. The tool path that has been set in a machining program not being used during automatic operation can be checked.

Direct entry of drawing dimensions

USB interface (2-PORT)

LAN port

Intelligent thermal shield

Intelligent safety shield

Mazak voice advisor

Virtual machining

Complete with: -

3 Driven Holders & 10 Static Holders

Second spindle C axis 0.0001° increments

Hi pressure coolant 15kg/213psi with temperature control

Workpiece unloader and conveyor

Hydrafeed multiservo 3-80 short magazine barfeed (Includes swing aside facility, Master spindle reduction liner to include 5 sets of reduction bushings and spacers, 3 push rods, coolant catcher) plus Hydrafeed bar support unit for 1.5m bar lengths – extends to headstock

Kitagawa BB206 170mm chuck for 1st spindle

Kitagawa BB206 170mm chuck for 2nd spindle

Hainbuch 65mm axfix collet with 10 round bore collets and changer head 1

Hainbuch 65mm axfix collet with 10 round bore collets and changer head 2 with gas spring ejector

Preparation for chip conveyor (side)

Chip conveyor (hinge) including chip bucket

NC controller, Cylindrical and polar co-ordinate

Special turret mounted second spindle parts collector

Machine Hours

Power on 5,911 hours

Auto Ope 2,884 hours

Auto cut 2,550 hours

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.