SPECIFICATION SHEET

# MACHINE		: - Used Harrison Alpha 330T Centre Lathe

Stock No		: - 8374

# PRICE			:

Serial No		: - D20007

Control		: -

Date of Manufacture	: - 2002

SPECIFICATION

Height of centres		167mm

Distance between centres	1000mm

Swing over bed			330mm

Swing over cross slide		210mm

Spindle bored to pass		40mm

Spindle nose			Camlock D1-4”

Taper in nose bush		No. 3MT

Spindle speeds			2 infinitely variable ranges

Low speeds			0-2000 rpm

High range			0-3500 rpm

Tailstock quill travel		110mm

Tailstock quill diameter		42mm

Tailstock quill taper		No. 3MT

Main motor			7.5kW

Complete with:-

3 Jaw chuck

Quick change toolpost and 12 0ff toolholders

Harrison/Fanuc Operator Screen

Lighting

Coolant system

Enclosed guarding

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.