SPECIFICATION SHEET

MACHINE			: - XYZ 200TC Slant Bed CNC Lathe

Stock No		: - 9206

# PRICE			: - £19,950.00 + VAT

Serial No		: - 0505002

Control			: - Siemens 810D Shop Turn

Date of Manufacture	: - 2004

SPECIFICATION

Swing over covers				420mm

Swing over carriage				330mm

Maximum machining diameter			200mm

X axis travel					180mm

Z axis travel					370mm

Spindle centre height from floor			920mm

Spindle nose					A2-6

Hole through spindle				62mm

Bar capacity					52mm

Front bearing (internal diameter)			100mm

Maximum spindle speed				4800rpm

Spindle motor power continuous/30 min		9kw/12kw

Max spindle speed for full power			1125rpm

X & Y axis rapid traverse rate			12 & 20 m/min

X & Z axis slideway configuration			Double Linear way

Ballscrew dia					32 x 32mm

Turret type					VDI 30

No of  tool stations				12

Turning tool dimension				20 x 20mm

Max boring bar dia				32mm

Tailstock quill taper				MT4

Quill Dia & Travel				75 x 100mm

Max quill thrust					795kg

Coolant tank capacity				115 litres

Coolant delivery 					50 litres/min @ 1.8 bar

Footprint					5,050 (with swarf conv & b/feed) x 1,800 x 2,100mm (h)

Approximate weight				2850kg

Complete with:-

Hydraulic 3 jaw chuck 210mm dia

Parts catcher

Toolsetter

Turret Tooling:

5 Turning Tool Holders

5 Drill/Boring Holders

3 Collet Chucks

Tailstock

Swarf conveyor

Interlocked guarding

Automatic lubrication system

Coolant system

CNC Control Manuals

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.