SPECIFICATION SHEET

# MACHINE		: - Mazak Variaxis 500 5 Axis Twin Pallet Machining Centre

Stock No		: - 9229

# PRICE			: - £49,500

Serial No		: - 160647

Control		: - Mazatrol PC Fusion 640M

Date of Manufacture	: - 2006

SPECIFICATION

Main Dimensions and Capacity

Max. Dimensions of workpiece - Diameter		Ф500mm		Ф19.69”

Height			405mm			15.94”

X-axis movement (saddle side to side movement)	510mm			20.08”

Y-axis movement (column side to side movement)	510mm			20.08”

Z-axis movement (head up and down movement)	460mm			18.11”

A-axis movement (table tilt)/0.001 deg indexing		-120 deg to +30 deg

C-axis movement (table rotation)/0.001 deg indexing	±360 deg

Distance from spindle end to table top

Table in horizontal position				190mm to 650mm	7.48” to 25.59”

Distance from spindle end to table centre

Table in vertical position				140mm to 600mm	5.51” to 23.62”

Table movable load (uniformly distributed load)		300kgf			6474.6lbs

Spindle

Spindle tapered bore					BT40

Standard specification (12000 minˉ¹ (rpm))

Spindle rotation speed					35 to 12000 minˉ¹ (rpm))

Spindle transmission range				Step-less

Spindle bearing internal diameter			80mm			3.15”

Main motor (AC inverter motor)

15 minute rating					22kW			30HP

Continuous rating					15kW			20HP

Feed Rate

Rapid feed rate X/Y/Z					50m/min 		164.1ft/min

Cutting feed rate X/Y/Z					50m/min 		164.1ft/min

Simultaneous control axis				3 axes in line

Index positioning time A				1.9sec/90deg

Index positioning time C				1.5 sec/90 deg, 2.1 sec/180deg

Table

Table dimension					Ф500 x 400mm width	Ф19.69 x 15.75” width

Table top surface (T-groove + reference hole)

Nominal dimension (ISO R299)				18mm			0.71”

Number of T grooves on the table			5

Interval							80mm			3.15”

Reference hole						Ф50mm +0.016		Ф1.97” +0.0006

Table top surface height (from upper surface of machine base)	800mm			31.5”

ATC Tool Magazine

Number of tools accommodated Optional		40

Tool selection system					Magazine pocket number random selection and 								automatic short-cut system

Tool shank						BT 40

Retention type						Yamazaki Ansi type

Maximum diameter of tool No conditions		Ф80mm		Ф3.15”

Maximum diameter of tool No adjacent tools		Ф125mm		Ф4.92”

Maximum length of tool (from the taper reference plane)	300mm			11.81”

Chip to chip time (MAS standard)

Less than tool weight 78N (171.6lbs)			4.5 sec

Maximum tool storage capacity of the whole magazine	Average 230kgf		506lbs

[5.8kg (12.76lbs) x 40 tools]

Maximum tool weight					8kg

Automatic Pallet Changer

Number of Pallets					2

Changer System					Rotary Type

Pallet change time					10.5 secs

Tank Capacity

Lubricating oil tank (for the slideway and spindle bearing)	3L			0.79gal (US)

Spindle cooling oil tank capacity			38L			10.04 gal (US)

Coolant tank capacity					300L			79.26 gal (US)

Accuracy

Positioning accuracy (pitch correction) X, Y, Z		±2.5μm 		±0.0001”

Positioning accuracy (pitch correction) A		±10 sec

Positioning accuracy (pitch correction) C		±5 sec

Repeated positioning accuracy X, Y, Z			±0.7μm			±0.000028”

Repeated positioning accuracy A			±5 sec

Repeated positioning accuracy C			±3 sec

Machine Size

Required floor area (including the chip conveyor)

Height (from the floor surface)				2842mm		111.89”

Depth							4300mm		169.29”

Length							3500mm		137.80”

(Includes 500mm for swarf conveyor)

Machine Weight					13,570kg

Power Supply

Power capacity

30 minute rating					46.7kVA

Continuous rating					36.4kVA

Total Cut Hours 7,627

Complete with:-

Renishaw Spindle probe

Through spindle coolant

Auto Toolsetter

Swarf conveyor

Manuals

Options switched on in the Control

EIA

Spiral

EIA 3D Comp

Rotation

Geometric

Scaling

Ext-Data I/O

High Speed

Shape Comp

Thread

Inverse Time

Auto TLM

Comparison Stop

Spline

G54.1

Sync Tapping

G00 Slope Const

Variable 600 Sets

Navigation

IC Card Running

EIA Helical Tap Cycle

Mazatrol Helical

Protocal B

Mazatrol Co-or Shift

Mazatrol Planet Tap

Auto Peack

Ethernet Running

Payment terms		: - In full prior to collection or delivery

Availability		: - Ex-stock subject to prior sale

Terms of trading	: - Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.