SPECIFICATION SHEET

# MACHINE		: - Used Haas Model VF3 Vertical CNC Machining Centre

Stock No		: - 8930

# PRICE			: - £24,950.00 + Carriage + VAT

Serial No		: - 22710

Control		: - Haas (Fanuc compatible) CNC Control system

Date of Manufacture	: - 2000

SPECIFICATION

Travel

X axis stroke				1016mm

Y axis stroke				508mm

Z axis stroke				635mm

Distance spindle nose to table		102-737mm

Table

Width					457mm

Length					1219mm

Max. Weight on table			1588kg

T Slots width				16mm

T Slots pitch				80mm

Spindle

Taper size				No.40

Speed					0-7500rpm

Bearings

Bearing lubrication			Air/oil injection

Cooling					Liquid cooled

Motor

Spindle motor, max. rating		14.9kW

Feedrate

Rapid X, Y & Z axis 			25.4m/min

Max. Cutting feedrate			16.5m/min

Toolchanger

Capacity				20 tools

Type					BT40

General

Approximate machine weight		5670kg

Air supply (min)			113lpm, 6.9 bar

Complete with:-

HRT 160 4th axis

Programmable coolant nozzle

Automatic lubrication system

Enclosed guarding

Swarf auger

Payment terms		: - In full prior to collection or delivery

Availability		: - Ex-stock subject to prior sale

Terms of trading	: - Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.