SPECIFICATION SHEET

# MACHINE	: - Nakamura WT150MMY

Stock No		: -  9014

# PRICE			: - £95,000 + VAT

Serial No		: - M154406

Control		: - Fanuc 18iT

Date of Manufacture	: - 2005 / Installed 2006

SPECIFICATION

Capacity

Swing over bed					190mm

Swing over saddles				190mm

Maximum turning diameter			190mm

Maximum turning length			400mm

Maximum bar size				51mm diameter

Main Spindle (Fixed left hand)

Spindle nose					A2-5

Drawtube bore diameter				52mm

Spindle power					15/11 kW

Spindle speed					5000rpm

Index angle (C axis)				0.001 degree

Second Spindle (Moving right hand)

Spindle nose					A2-5

Drawtube bore diameter				52mm

Spindle power					11/7.5 kW

Spindle speed					5000rpm

Index angle (C axis)				0.001 degree

Top Turret/Bottom Turret

Type						Base tool holder

Number of stations				12

Number of turret index positions		24

OD tool size					20mm square

Boring bar size					32mm diameter

Rotary tool power				3.7kW

Rotary tool speed				6000rpm

Axis Travel

X axis (top turret)				172.5mm

X axis (bottom turret)				172.5mm

Z axis (top turret/bottom turret)			465mm

Y axis (top turret)				+/-35mm

Rapid Traverse

X axis (top turret/bottom turret)			16000mm/min

Z axis (top turret/bottom turret)			40000mm/min

Y axis (top turret)				6000mm/min

Sub spindle					40000mm/min

C axis (left/right hand spindles)			600rpm

Machine Services

Power requirement				67kVA

Air pressure					6kgf/cm²

Machine Dimensions

Machine weight					8500kg

Machine floor space				2860mm x 2190mm

Complete with:-

Left hand/right hand spindle synchronization

Manual detachable tool setter (top and bottom turret)

Fully enclosed splashguard

Automatic lubrication unit

Lighting

RS 232 socket

Transformer

Parts catcher type A, left and type B, right with internal parts conveyor

1 x collet chuck, Hainbuch – Left spindle

1 x 3-jawchuck, SMW Autoblock – Right spindle

toolholder package: 6 x driven (3 x radial + 3 x axial), 18 x static

1 x barfeeder, LNS Quick Load Servo 3

Swarf conveyor

2 x high pressure pumps 20 bar, Grundfoss

CE Marked

Full set of machine manuals

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.