SPECIFICATION SHEET

# MACHINE		: - Used Mazak Quickturn Smart 350

Stock No		: - 9280

# PRICE			: - £83,500.00 + VAT

Serial No		: - 228152

Control		: - Mazatrol Smart

Date of Manufacture	: - 2012

SPECIFICATION

Capacity

Chuck size						12 in

Maximum swing					ɸ720mm

Machining diameter (STD)				ɸ254mm

Machining diameter (MAX.)				ɸ420mm

Centre distance						1250mm

Bar work capacity					ɸ102mm

Distance between spindle end and turret end face	142 to 1442mm

Max. support mass (chuck include)

Chuck work						650kg

Shaft work						1000kg

Spindle

Spindle speed 						35 to 3300 minˉ¹

Spindle end face					JIS A2-11”

Acceleration time					4.3s

Spindle through hole					ɸ112mm

Motor output (30 min./cont.)				30/22 kW

Maximum torque					808N·m

Tailstock

Centre bore 						MT No. 5

Travel (tailstock)					1265mm

Minimum thrust					1000N

Maximum thrust					10000N

Turret

Number of tools					12 pieces

Tool size

Outside turning						□25mm

Inside turning						ɸ50mm

Indexing time one/full					0.2/0.6s

Feed Axes

Rapid traverse X/Z					30/33m/min

R. T time constant X/Z					80/70ms

Travel X						240mm [235 + 5]

Travel Z						1305mm [1300 + 5]

Others

Coolant tank capacity Discharge CV (without/side)	300/350L

Power requirement (cont./30min.)			43.1/54.5kVA

Total

Overall dimensions					4900 (incl. swarf conveyor) x 2100mm

Machine weight						6900kg

Complete with:

BB212 305mm chuck

Toolsetter

Tailstock

Turret Tooling

Swarf conveyor

Manuals

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power.

Every effort has been made to ensure the above specification is accurate,

however we advise you to check critical criteria.