SPECIFICATION SHEET

# MACHINE		: - Used Colchester Combi K4 CNC Combination Lathe

Stock No		: - 9653

Price			: - £17,500 + Carriage + VAT

Serial No		: - C50046

Control		: - Fanuc 210i TA CNC Control

Date of Manufacture	: - 2004

SPECIFICATION

Swing over bed			554mm

Swing in gap				830mm

Swing over cross slide		370mm

Distance between centres		1016mm

X axis cross slide travel		290mm

Spindle nose (Camlock)		D1-11

Spindle bore				102mm

Spindle motor				18.5/22kW

Spindle speeds (programmable)	4-1800rpm

X axis ballscrew, diameter x pitch	25 x 4mm

Z axis ballscrew, diameter x pitch	40 x 10mm

Tailstock quill taper			No. 6 MT

Tailstock quill travel			145mm

Bedway width (30-degree slant)	405mm

Approximate nett weight		3650kg

Complete with:-

315mm Chuck

8 station VDI turret

Guarding

Coolant system

Lighting

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.