SPECIFICATION SHEET

# MACHINE		: - Used Colchester Tornado 220 CNC Slant Bed Production Lathe

Stock No		: - 9654

Price			: - £17,500.00 + Carriage + VAT

Serial No		: - T40012

Control		: - Fanuc 21i-TB CNC Control System

Date of Manufacture	: - 2001

SPECIFICATION

Maximum swing			510mm

Maximum turned diameter		260mm

Maximum turning length		540mm

Bed inclination				60 degrees

Spindle centre height (from floor)	960mm

Spindle nose				A2-6

Power chucking system			Hydraulic

Spindle bore				77.5mm

Bar capacity – collet			65mm

Maximum spindle speed		5000rpm

Spindle motor power			22kW

Rapid traverse: Z/X Axis		30/25m/min

Turret:	Tooling type			VDI 40

Number of tooling stations		12

Approximate net weight			4450kg

Complete with:-

Hydraulic tailstock

Coolant system

Lighting

Interlocked guarding

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.