SPECIFICATION SHEET

# MACHINE	: - Used Tongtai TA20LMB Driven Tool Sub Spindle Turning Centre

Stock No		: - 9846

# PRICE			: - £29,750.00 + Carriage + VAT

Serial No		: - U20195

Date of Manufacture	: - 2012

Control		:- Fanuc 18i-TB

SPECIFICATION

Capacity

Swing diameter			ø450mm		17.7”

Maximum workpiece diameter	ø334mm		13.1”

Maximum workpiece length		650mm		26.6”

Chuck size main/sub			ø210mm		8”

Sp. Through bar			ø51mm		2”

Spindle - Main

Maximum rotation			4,500rpm

Front spindle diameter		ø100mm

Front nose				A2-6

Through hole				ø62mm

Maximum power rating		22/18.5kw

Maximum torque			307Nm

Basis rotation				575rpm

Motor type (belt)			αP40/6,000i

Spindle – Sub

Maximum rotation			4,500rpm

Front spindle diameter		ø90mm

Through hole				ø35mm

Maximum power rating		7.5/5.5kw

Maximum torque			48Nm

Basis rotation				1,500rpm

Motor type (built in)			αB112M/15,000i

Feed Drive

Travel			X axis		260mm		10.24”

Z axis		650mm		16.5”

Rapid feed rate	X axis		30m/min

Z axis		30mm

Servo motor 		X axis		4.0 kw (α22/3,000i) + BR

Z axis		3.0 kw (α12/3,000i)

Ball screw size 	X axis		ø 32*10mm

Z axis		ø 32*12mm

Linear guide size	X axis		ø 35mm

Z axis		ø 35

Tooling System

Tool shank type			VDI-40

Station					12

Tool shank size	OD		ø25mm

ID		ø 40mm

Index & live tool motor		5.5/3.7kw (α3/10,000i)

Live tool maximum rotation		4,000rpm

Live tool maximum torque		35Nm

Hydraulic

Motor					1.5kw

Tank					30l

Coolant

Motor 					0.37kw

Tank					170l

Machine Size

Width x Length x Height		6500 (including barfeed & swarf conveyor) x 2100 x 2155

Weight					5,500kg

Complete With

Short mag barfeed

Collet chucks main and sub spindle + 1 collet in each

Parts catcher and conveyor

3 driven holders and static tooling

Swarf conveyor

Manual

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.