SPECIFICATION SHEET

# MACHINE	: - Used Haas Model VF3 SS High Speed Vertical Machining Centre

Stock No		: - 9939

# PRICE			: - £59,950.00 + Carriage + VAT

Serial No		: - 1072651

Date of Manufacture	: - 2008

Control		:- Haas CNC control

SPECIFICATION

Table size			1219mm x 457mm

X axis traverse		1016mm

Y axis traverse		508mm

Z axis traverse		635mm

Spindle nose to table		102-737mm

Spindle			BT 40

Spindle speeds		0-12000rpm

Spindle motor			22.4kW

Rapid feed rate		35.6m/min

Toolchanger capacity		40 + 1 tools

Approximate weight		5670Kg

Complete With

Nikken 5A201 5th axis (New 2013)

Through spindle coolant

Renishaw toolsetting and spindle probes

Swarf auger

Assorted BT 40 toolholders

Programmable coolant nozzle

Lighting

Guarding

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.