SPECIFICATION SHEET

# MACHINE	: - Used Haas Model VF2 SS YT Vertical Machining Centre

Stock No		: - 9994

# PRICE			: - £64,950.00 + Carriage + VAT

Serial No		: - 1152478

Date of Manufacture	: - 2018

Control		:- Haas

SPECIFICATION

Table size			914mm x 457mm

X axis traverse		762mm

Y axis traverse		508mm

Z axis traverse		508mm

Spindle nose to table		102-610mm

Spindle			BT 40

Spindle speeds		0-12000rpm

Spindle motor			22.4kW

Rapid feed rate		35.6m/min

Toolchanger capacity		30 + 1 tools

Approximate weight		3629Kg

Complete With

Swarf auger

Haas HRT 160 4th Axis table plus A frame support

Through spindle coolant

Auxillary Filter

Wireless intuitive probing system

Programmable coolant nozzle

Lighting

Guarding

Payment terms	:- In full prior to collection or delivery

Availability	:- Ex-stock subject to prior sale

Terms of trading	:- Please refer to our standard terms and conditions of trading attached.

This machine can be seen under power at our premises in Burgess Hill.  Every effort has been made to ensure the above specification is accurate, however we advise you to check critical criteria.